Final Report

2002 Reduced Gravity Student Flight Opportunities Program

Gr.A.I.N.S.

Granular Agglomeration in Non-gravitating Systems

Experiment 2002-035

November 1, 2002

The University of Tulsa Granular Dynamics Group

Department of Physics and Engineering Physics

The University of Tulsa

600 South College Avenue

Tulsa, OK 74104

Investigators:

Jeremy Cain, Aaron Coyner, Whitney Marshall, Adrienne McVey,

Justin Mitchell, Matthew Olson, and Rebecca Ragar

Former Faculty Advisor:

Dr. Michael Wilson

Current Faculty Advisor:

Shawn Jackson

# Technical Aspects

## Experimental Abstract

Recently, a great deal of effort both industrially and academically has focused on studying the interactions within and overall behavior of granular systems (Jaeger).  Of particular interest have been studies of ‘gases’ of macroscopic objects such as ball bearings, dust, soot, etc.  Theoretical models have predicted (Grossman) and some experiments have shown (Maddox) that a gas of balls tends to cluster when the gas is undisturbed by external influences, such as gravity.  The behavior of such clusters appears to be dependent on driving conditions, particle densities and coefficients of restitution of the balls.  In 2D experiments the motions of individual balls have been analyzed; where as in 3D systems this has not yet been done.  The only 3D experiment performed was on a set of fairly dense systems (Falcon).  The density was high enough that correlation could not be made between collapse of the gas, particle energies, input energies, and effective gas pressure.

The question of collapse has particular importance for a description of the dynamics of interstellar dust clouds and planetary ring systems (Jaeger).  Measurements of asteroid densities have shown that objects less than about (1km)3 in volume have densities on the order of 1-1.5 g/cm3 (Yeomans).  At these densities, an object 100 meters in radius has an escape velocity of ~1 cm/s.  With such small escape speeds these objects are not able to gravitationally accumulate mass and thus are not able to accrete dust and grow in size.  Inelastic collapse, if it is shown to occur in dilute dusty systems, would provide an impetus for the formation of these moderately sized objects.

In this project we aim to examine the occurrence and dynamic behavior of a gas of small particles, which is expected to show strong evidence of clustering.  This project will utilize an apparatus currently being constructed by our group at The University of Tulsa for the study of granular dynamics aboard the Space Shuttle.  With minor changes, this system will be used to monitor, probe, and verify the behaviors predicted for granular clustering.

## Test Procedures

Due to the difficulty of manually carrying out complicated experimental procedures in a microgravity environment, and since this experiment will eventually fly aboard the Space Shuttle via the Get Away Special Program, the apparatus was designed to facilitate a highly-automated data collection process.  During the actual flight, crew members were responsible for powering up experimental equipment before the first zero-g maneuver, pressing a button before each zero-g maneuver to advance between experiments, and powering down the experiment upon the completion of the last parabola, in addition to dealing with any unforeseen problems.  The following list describes the procedures followed before, during, and after both flights.

### Pre-Flight:

- Verify all experimental systems functioning properly:

  - DC shaker motor

  - Stepper motor

  - Shaker system

  - Lights

  - Camera

  - User interface

  - Power supply

- Verify proper optical alignment of cameras and mirrors.

- Change video tapes (Flight day 2 only).

### Flight

- Retrieve power supply from stowed position and strap down with RGSFOP-provided straps.

- Connect power supply to experiment and turn on.

- Power up experiment.

- Use IR remote to start camcorders recording.

- Approximately 10 seconds before entering microgravity, depress NEXT button to advance to experiment 1.  Microcontroller runs the preprogrammed experiment 1.

- For each subsequent maneuver, approximately 10 seconds before microgravity entry, depress NEXT button to advance to the next experiment.

- Following last microgravity parabola, power down experiment.

- Turn off power supply and disconnect from experiment.

- Unstrap power supply and return to crash-proof box for landing.

### Post-Flight

- Review collected data.

- Note any deviations from planned data collection.

- Note any problems with experimental apparatus or procedures.

The plan for data collection was to run the same set of 40 experiments on both flight days.  Difficulties with the experiment’s electrical system made it possible to collect only 1 parabola worth of data on the first day.  On the second flight, both crew members were incapacitated with motion sickness for approximately half the flight.  As a result only 23 experiments were run the second day.

# Data Collection and Test Results

## Brief Review of Apparatus

The experimental system in the GrAINS apparatus consists of a box separated into eight sections of equal size, each filled with a different number of brass ball bearings.  The box is shaken along a body diagonal at various amplitudes and frequencies.  Piezoelectric pressure sensors collected information about ball collisions into one wall of each box.  These sensors will be discussed later at length.  The pressure sensor data and all visual information were recorded into JVC camcorders.  Pressure information was recorded in the camera’s audio channels.  The audio data contains collision information and are analyzed using audio techniques such as Fourier Transforms.

## Data Collection and Preparation

Four sets of impact sensor readings were recorded for 21 microgravity parabolas on our second flight day.  Our sensors consist of a 1mm thick sapphire plate epoxied to one side of a piezoelectric disk.  On the opposite side of the disk was epoxied a 1 mm thick lead sheet.  The lead acts as a rigid surface ensuring that impacts to the sensor will cause deformation of the disk and not movement of the entire sensor assembly.  Epoxied to the lead is a 1.5 mm thick layer of foam rubber that is glued to the aluminum support frame.  The rubber and lead act as a vibration mass damper and were selected to attenuate most high frequency mechanical impulses present in the aluminum frame.  In this fashion, balls impacting the sapphire plate transmit acoustic pulses into the piezoelectric disk resulting in a measurable voltage spike.

Sensor data were recorded by electrically connecting the piezoelectric disks to the audio inputs of the cameras used to record the experiment.  Each camera has two independent digital audio input channels (left and right).  These channels record 16-bit audio at a sampling rate of 48 kHz.  The independent audio channels allow us to record data from two sensors on each camera.  One of our cameras failed to operate during the second flight.  Thus, we have data for only four of our eight sample cells. The four sample cells are filled with varying numbers and sizes of brass balls (data presented in table 1). This information allows us to compare the audio data, and analyze the effect of ball size and packing density on our recorded signals.  One dilemma in the analysis has been that our control cell, an empty chamber, was wired to the failed camera.  As a result, we do not have a ‘no impact’ data set to use as a baseline comparison for the filled sample chambers.  Our experiment was also unable to record usable data on the first flight due to an electrical problem within our system.

| Sensor | Data Channel | Cell Filling |
| --- | --- | --- |
| E | #1 L | ~250: 1mm diameter |
| C | #1 R | ~10000: 0.5 mm diameter |
| B | #2 L | ~775: 1 mm diameter |
| D | #2 R | ~387: 1mm diameter ~1600: 0.5 mm diameter |

Table 1: Data Channel and Cell Filling for each recorded piezoelectric sensor.

Once on the ground, the video/audio data sets were read off digitally via each camera’s Firewire port and stored in .avi format.  These sets were the processed using Adobe Premiere® to create stand-alone .wav audio files.  These .wav files were then processed using SpectraPlus FFT analysis software.  The .avi files were converted into a series of bitmap files, which are being analyzed using software we are developing using the Interactive Data Language (IDL).  All testing data were recorded and processed using the same sequence of steps.

## Analysis Procedures and Results

### Camera Audio Testing

Preliminary work needed to analyze and interpret our impact sensor data was focused on determining the Sensor Response Function (SRF), thus correlating input signal voltages with the recorded values.  Pre-flight studies centered on a large-scale frequency dependence and noted a slow reduction in the recorded signal when the frequencies were lowered below ~100 Hz.  A more thorough frequency response determination was initiated post-flight.  This test showed the perplexing result that there exist extremely narrow frequency bands of strong signal attenuation.  Data measured for a constant 300 mV AC signal is shown in Figure 1.

Strong signal attenuation is observed with a fundamental frequency of 150 Hz.  The bandwidth of the attenuated signals is observed to be significantly less than the 10 Hz point spacing of the data set.  Additional data will be taken to more thoroughly investigate these attenuation bands.  Overall, the attenuated bands do not constitute a significant fraction of the frequency range examined and for our first analysis we ignored these loss bands and assumed a flat frequency response for signals greater an 50 Hz.

An additional problem discovered during the testing phase was apparent coupling between the audio channels.  This coupling appears highly nonlinear and is most prevalent at high frequencies (>1500 Hz).  Since much of the structure we see in the data sets involve the low frequency range, we have continued analysis of that range until we can resolve the coupling issue.  We continue to work on possible solutions to work around the coupling hindrance while also researching other means of data storage to eliminate the problem from potential future flights.

Figure 1: Measured audio channel rms voltage (Vcam) divided by the input rms voltage (Vapp) plotted versus the applied frequency.

### Visual Testing

The software currently being developed was tested on two-dimensional simulations done by Marshall of this group.  The simulations were of white balls on a black background.  Being in three-dimensions and in a lower contrast situation has proven difficult, but not impossible.  While the software originally input .jpeg files, the need for uncompressed graphics was apparent and the conversion to bitmaps has taken more time than was expected.  Figure 2 is an example image from one of Marshall’s simulations.

Figure 2: Still image from two-dimensional simulation used to design analysis software.

### Flight Data

While there are still unresolved issues from the SRF, we pushed on with analysis of the audio flight data to determine what information could be discerned.  The first noticeable structure was the existence of two periodic frequencies.  One, shown in Figure 3, is a very low frequency clustering of many high frequency signals.  The periodicity of this envelop matches the driving frequency of the system to within the tolerances of the driving motor, and we argue is due to a measured signal as the wall of the sensor is periodically pushed into the ‘gas’ of granular particles.  An advancing wall will experience a high number of collisions in a short time period while a retreating will experience relatively few.

Figure 4 shows clusters of high frequency peaks separated by on average ~0.082 seconds during flight parabola 7.  This corresponds to an average frequency of 12.2 Hz.  Our microprocessor data for parabola 7 showed an average frequency of 12.03 Hz with a standard deviation of 0.64 Hz.  Similar correlation is seen in analyzing all other data sets.

Figure 3: Excerpt from Camera 2 Parabola 7 time series

The second frequency appears with a ‘push’ of the wall.  We see a high frequency interposed on the data.  This high frequency periodicity is shown in Figure 4.  Although most clearly evident in the left channel plot of Figure 4, all data sets appear to have the same high frequency periodicity.  The peaks in the time series indicate a frequency of just less than 500 Hz. In figure 4, the periodic signal shows more defined peaks and higher voltage levels. Our current belief is that these higher voltage peaks are a result of interactions between the sensor and the larger diameter balls in box b (left channel). The data for box d (right channel) shows for the most part a very low signal but occasionally shows slightly higher voltage peaks. The variation in form and size of voltage peaks is thought to be a result of the varying ball sizes within the cell.

Figure 4: Excerpt of time series from Camera 2 Parabola 9.

The high frequency signal proved the most straightforward to analyze.  A FFT analysis based on one data set is shown in Figure 5.  This clearly shows a comb of multiple harmonics, the fundamental frequency of which is 474.7 Hz.  We are currently attributing this signal to RF interference from a stepper motor used in the system, although this link has yet to be properly established.  Testing is ongoing.

Figure 5: FFT spectrum of typical audio data file.  This spectrum was taken from Camera 2 Parabola 7.

Of greater interest to our analysis of ball impacts have been studies of the low frequency ‘clumped’ signals shown in Figure 5.  The FFT routine used to describe the high frequency components has been ineffective at analyzing the low frequency signal.  This was due to insufficient resolution in the FFT routine.  The FFT program was limited to a 32,758 Hz sampling rate.  When used to analyze our 48 kHz data, we found the limiting frequency separation to be ~15Hz.  Unfortunately, this scale is on the same order of magnitude as the frequencies we are trying to measure.

To work around this issue, we have parsed our data sets in an effort to increase the time interval sampled by the FFT routine.  Increasing the time interval allows the FFT to obtain finer frequency spacing and thus a more detailed spectrum.  In our first attempt, the data sets have been parsed into six subsets, each set containing every 6th point of our complete data set.  This procedure has reduced the frequency separation to 2.5 Hz.  The six resulting data sets were individually processed by the FFT software and then averaged to obtain the parsed spectrum shown in Figure 6.  The parsed spectrum shows a 10-20 dB increase in amplitude at frequency between 0 and 50 Hz.

Figure 6: Plot of parsed and unparsed spectra amplitudes (dB) versus frequncy.

Significant low frequency structure is now apparent in the data.  The data still lack sufficient resolution for quantitative analysis of the low frequency signals.  As we learn more about the pitfalls of parsing we expect to be able to fully analyze these low frequency components and gain vital information about the gas density and cloud momentum as the wall is moved through the cloud of balls.

The GrAINS campaign collected considerable video data.  Figure 7 is an example frame from the video.  We did experience some difficulties, which will be discussed later.  There are two main goals for this video information.  The first is to find a speed distribution of a collection of brass beads shaken in a microgravity environment.  The second is to show inelastic collapse of this ensemble.  The collapse is theorized to be a clumping of macroscopic particles due to many successive inelastic collisions and could be a factor in the formation of planetary rings, asteroids, comets, planets, avalanches, sand dunes and may other granular ensembles.

Figure 7: Frame taken from digital movie file.  Some balls are obviously hidden because the system is three-dimensional.  The white disks are piezoelectric sensors.

The speed distribution is scientifically interesting because of its scale.  Were we considering a system of two balls or a system of 1023 balls we would already have sophisticated theoretical models to describe the system’s behavior.  In our system, on the order of thousands of beads, we cannot make all the statistical simplifications of gaseous behavior nor can we make simple collision arguments for every bead.  A speed distribution function would be a crucial step in describing these sorts of systems.

We will soon meet our particle tracking and speed distribution goal.  Though we do have considerably less video than we hoped, we still have more low gravity video for this type of system than any group known to us in the world.

The ongoing video analysis project employs the Interactive Data Language (IDL).  This programming language is commonly used in video analysis and includes built-in routines to assist particle finding.  Currently, we have the ability to find balls in a given video frame, but the accuracy is not yet known.  The program makes a contour, or gradient, of each video image.  A ball’s contour will look like a circle.  Figure 8 is an example of such a contour created in Adobe Photoshop.  Figure 9 is a close up of the lower right box containing the smallest beads.  The small balls are now easier to see than before and are easy for IDL to find.  The program finds the center of these circles, which we take to be the center of the balls.  Combining the ball location information from successive video frames will allow us to find the speed of every ball in the frame at any time during the video.  A histogram of these speeds will constitute a graph of the speed distribution.

Figure 8: The figure is a contoured image of our system.  The balls are much easier to see now and focusing has less of an effect.

We have considered some problems with this method of finding the speed distribution.  We can only find the speed of balls in the camera’s field of view.  Because the system is three-dimensional we cannot determine the distribution of low speeds.  Balls can easily obscure each other.  Unfortunately, the fastest balls near the outside walls likely obscure the slowest moving balls in the system.  This problem of overlapping balls is obvious in Figure 6.  More importantly, our cameras experienced unexpected focusing problems.  Originally, we thought the poor focusing would be devastating to our efforts to track the balls.  Fortunately, focusing affects the original image much more than the contoured image.

Figure 9: The small circles represent the smallest of our brass ball bearings.  They are much easier to see than in Figure 6.

Though we have not yet completed our original goals, we have met peripheral goals.  We quickly noticed that random KC135 accelerations greatly affected some shaking parameters, but not others.  This has shown us the minimum energy needed to keep the balls in a “gaseous” state.  We have a phase diagram that shows when we have generally gaseous behavior and when the balls all fall to one corner.  This diagram is shown in Table 2.

|  |  |  |  |  | Frequency(Hz) |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | 8 | 9 | 10 | 12 | 15 | 16 | 17 | 18 | 21 |
|  | 0.84 | no gas | no gas |  | no gas | Gas |  |  |  |  |
| Amp(mm) | 0.78 | no gas | no gas |  | Gas | Gas | Gas |  |  | Gas |
|  | 0.73 |  | no gas | no gas | no gas |  | Gas | Gas |  | Gas |
|  | 0.61 |  |  | no gas | no gas | Gas |  | Gas | Gas |  |

Table 2: Phase diagram of ball behavior.

We have had less success in determining conditions for inelastic collapse.  Our current thinking is that we underestimated the KC135’s random accelerations.  Thus, any clusters that would have formed were torn apart by either plane accelerations or high shaking amplitudes and frequencies.

All other difficulties have been relatively minor.  We did have problems with excessive light on one of our cameras from a near by experiment.  The flood of light enhanced focusing our focusing problems and caused the camera to use much more power than it otherwise would.

### Continuing Work

As noted above, the impact sensor data analysis is still in its early stages.  In the coming months we will get a better handle on the Sensor Response Function as well as the origin of the high frequency periodic signal.  There is good information to be gained through this data set.  Additionally, we are learning how this system would be improved for a potential second flight opportunity.

We can now find balls.  The next task is to find their speeds.  We have most of the software written to do this and will be making progress towards this aim in the coming weeks.  We are still investigating ways to retrieve information about possible clumps, but we may not have any because of KC135 vibrations and accelerations.

# OUTREACH

The goal of the GrAINS outreach program is to share with the Tulsa community, as well as others via the World Wide Web, the scientific findings of the experiment, as well as the unique experience provided team members by NASA’s Reduced Gravity Student Flight Opportunities Program.  This has been achieved through several presentations around the Tulsa area and beyond, newspaper articles written by the team journalist, TV interviews, and a comprehensive website.

In the interest of documentation, an “electronic scrapbook” with scanned copies of newspaper articles, advertisements, and various other relevant publicity items has been included with this report.  A video scrapbook was compiled and included.  The contents of the video scrapbook are as follows:

| Date | Length | Description |
| --- | --- | --- |
| September 19, 2002 | 18 min | Video of presentation to Broken Arrow High School |
| July 29,2002 | 3 min. | Television interview on KJRH channel 2 (local NBC affiliate station) |
| Fall 2002 | 30 sec. | University of Tulsa commercial aired on several local stations |
| July 22 and 23, 2002 | 20 min. | Edited video of flights |

All team members have been involved in presentations to various groups in Tulsa and the surrounding areas.  In these presentations, they describe the experiment, display and explain the function of the apparatus, discuss the scientific findings, and show video footage of the flight.  In addition, members of the flight crew are able to share their personal experiences aboard the KC-135.  While the basic format of all the presentations is similar, they are tailored to the age and scientific background of the particular group.  For example, when talking to young children, team members do a demonstration with a large-scale mock-up of the experiment to help the children gain a better understanding of the underlying scientific concepts.  The following table lists the presentations completed to date, as well as those planned for the future.

| Date | Presentation to | Audience | Number of Attendees |
| --- | --- | --- | --- |
| August 15, 2002 | Van Buren Rotary Club – Van Buren, Arkansas | Local professionals | 34 |
| September 13, 2002 | Union High School Young Astronauts Program – Tulsa, Oklahoma | High School students and faculty | 18 |
| September 18, 2002 | Moore Elementary School – Tulsa, OK | Fifth grade Gifted and Talented class | 30 |
| September 19, 2002 | Broken Arrow North Intermediate High School – Broken Arrow, OK | Ninth grade Physical Science class | 2 classes of 30 students each |
| September 20, 2002 | Broken Arrow High School – Broken Arrow, OK | AP Physics class | 9 |
| September 20, 2002 | Astronomy Club of Tulsa –Tulsa, OK | Local teachers and amateur astronomers | 60 |
| September 26, 2002 | Tulsa Air and Space Center – Tulsa, OK | Educators from Starbase Oklahoma Project | 15 |
| September 28, 2002 | Society of Women Engineers Brownie Day – University of Tulsa | Brownie and Girl Scout Troops | 120 |
| October 16, 2002 | The University of Tulsa Society of Women Engineers | TU engineering students | 26 |
| November 24-26, 2002 | American Physics Society Division of Fluid Dynamics Meeting 2002 – Dallas, TX | Professional and student physicists |  |
| February 3, 2003 | Tulsa Engineering Society Meeting | Professional engineers in the Tulsa Area. |  |

The goal of the presentations to elementary, junior high, and high school students was to cultivate heightened interest in space science within those age groups.  The goal was realized through classroom presentations as well as the Society of Women Engineers Brownie Day, which presented an opportunity to reach approximately 120 young Girl Scouts.

As a result of the presentation to the Union High School Young Astronauts, the GrAINS research team has formed an ongoing cooperation with that organization.  The team now meets with the Young Astronauts bimonthly to assist the younger students with developing a self-contained experiment for inclusion in possible future RGSFOP flights.

In addition to direct presentations to students, the GrAINS outreach program has further impacted youth via presentations to educators.  The hope is that these presentations will excite teachers and provide them with material relevant to space science to discuss in the classroom.

The presentation to the University of Tulsa chapter of the Society of Women Engineers allowed the team to educate fellow TU science and engineering students about the experiment and the remarkable opportunity provided to undergraduates by the RGSFOP.  Because of the engineering backgrounds of this particular audience, the presenters were able to go into some detail about the scientific background, as well as the results, of the experiment.

Presentations to professional societies are another key part of GrAINS outreach.  Two team members, Justin Mitchell and Aaron Coyner, will give a 15-minute oral presentation about the GrAINS project at the American Physics Society Division of Fluid Dynamics Meeting in November 2002.  At the convention, which will be held in Dallas, they will briefly discuss the design of the apparatus, as well as present the results of the experiment. A presentation to the Tulsa Engineering Society is planned for February 2003.

The project has had two interviews that have aired on a local TV station during the 6pm and 10pm broadcasts, the first of which covered the purpose of the project and what we were doing to build and test our apparatus.  The second interview documented our trip to Houston and can be viewed as the second video clip in our video scrapbook.

The team journalist, Shaun Shafer, is a staff writer for the Tulsa World.  Three of his GrAINS-related articles were published in the newspaper.  All three articles are included in the electronic scrapbook, and text-only versions are linked from the project website.  The March 27th and May 26th articles ran before the flight took place.  These stories, which provided scientific background and followed the experiment through its formative stages, served to inform the community of the project and its purpose and to stimulate interest.  The latest article was published on July 28th, the week after the team’s return from Houston, and includes descriptions of, and pictures from, the microgravity flight and the rest of the team’s time at NASA.

The project website is regularly updated with the most current information about the experiment.  Contents include the text from the Tulsa World articles, links to photographs of pre-flight activities and the flight, and a link to a short article about the experiment on the University of Tulsa website.  In addition, an entire page is devoted to outreach, listing the presentations already completed as well as team member contact information for any groups interested in a presentation.  The website URL is: http://www.granular.utulsa.edu/GRAINS.html.